## Slide 1: IP Addressing

## Slide 2: Table of Contents
IP Terminology
The Hierarchical IP Addressing Scheme
IPv4 Address Types
Network Address Translation (NAT)
Internet Protocol Version 6 (IPv6)

## Slide 3: IP Terminology
1

## Slide 4: IP Terminology
Octet - Same as byte, made up of 8 bits
Network Address - This is the designation used in routing to send packets to a remote network—for example, 10.0.0.0, 172.16.0.0, and 192.168.10.0.
Host Address - A logical address used to define a single host
Broadcast Address - Used by applications and hosts to send information to all hosts on a network. For example 255.255.255.255, which designates all networks and all hosts
Notes: Sekizli - 8 bitten oluşan bir sekizli, sıradan bir 8 bitlik ikili sayıdır.
Ağ Adresi - Bu, paketleri uzak bir ağa göndermek için yönlendirmede kullanılan atamadır;
örneğin, 10.0.0.0, 172.16.0.0 ve 192.168.10.0.
HOST Adresi - Tek bir ana bilgisayarı tanımlamak için kullanılan mantıksal bir adres; ancak,
IP adresleri ana bilgisayarların çoğuna veya tümüne başvurmak için de kullanılabilir.
Yalnızca IP olarak yazılmış bir şey görürseniz, bu IPv4'e atıfta bulunmaktadır. IPv6 her zaman IPv6 olarak yazılacaktır.
Broadcast Adresi - Yayın adresi, uygulamalar ve ana bilgisayarlar tarafından bir ağdaki tüm ana bilgisayarlara bilgi göndermek için kullanılır.
Örnekler arasında, tüm ağları ve tüm ana bilgisayarları belirleyen 255.255.255.255;
172.16.0.0 ağındaki tüm alt ağları ve ana bilgisayarları belirten 172.16.255.255;
ve 10.0.0.0 ağındaki tüm alt ağlara ve ana bilgisayarlara yayın yapan 10.255.255.255.
Octet - An octet, made up of 8 bits, is just an ordinary 8-bit binary number.
Network Address - This is the designation used in routing to send packets to a remote network—for example, 10.0.0.0, 172.16.0.0, and 192.168.10.0.
IP Address - A logical address used to define a single host; however, IP addresses can be used to reference many or all hosts as well. If you see something written as just IP, it is referring to IPv4. IPv6 will always be written as IPv6.
Broadcast Address - The broadcast address is used by applications and hosts to send information to all hosts on a network. Examples include 255.255.255.255, which designates all networks and all hosts; 172.16.255.255, which specifies all subnets and hosts on network 172.16.0.0; and 10.255.255.255, which broadcasts to all subnets and hosts on network 10.0.0.0.

## Slide 5: The Hierarchical IP Addressing Scheme
2

## Slide 6: The Hierarchical IP Addressing Scheme
IP address consists of 32 bits or 4 bytes or 4 octets
Represented as:
  54.164.151.235 or
  00110110.10100100.10010111.11101011 or
  66.A4.97.EB
32-bit IP address is structured (or hierarchical) address to make routing possible
If IP address was flat (or non hierarchical) routing would be impossible
Notes: An IP address consists of 32 bits of information. These bits are divided into four sections, referred to as octets or bytes, and four octets sum up to 32 bits (8 × 4 = 32).
You can depict an IP address using one of three methods:
  Dotted-decimal, as in 172.16.30.56
  Binary, as in 10101100.00010000.00011110.00111000
  Hexadecimal, as in AC.10.1E.38
Each of these examples validly represents the same IP address. Hexadecimal is used with IPv6, and IP addressing uses dotted-decimal or binary.
The 32-bit IP address is known as a structured, or hierarchical, address as opposed to a flat, or nonhierarchical, address. Although either type of addressing scheme can be used, hierarchical addressing has been chosen for a very important reason. The major advantage of this scheme is that it can handle a large number of addresses, namely, 4.3 billion (a 32-bit address space gives you 2^32 , or 4,294,967,296). The disadvantage of the flat-addressing scheme and the reason it's not used for IP addressing relates to routing. If every address were unique, all routers on the Internet would need to store the address of each and every machine on the Internet. This would make efficient routing impossible, even if only a fraction of all possible addresses were used.

## Slide 7: The Hierarchical IP Addressing Scheme
The network address (or network number) uniquely identifies each network
Every machine on the same network shares that network address as part of its IP address
For example:
IP Address:
154.101.
51.235
Network address: Every device in this network starts with these numbers
Host address
Notes: Ağ numarası olarak da adlandırılan ağ adresi, her ağı benzersiz şekilde tanımlar.
Aynı ağdaki her makine, bu ağ adresini IP adresinin bir parçası olarak paylaşır.
Örneğin 172.16.30.56 IP adresinde, 172.16 ağ adresidir.
Ana bilgisayar adresi, bir ağdaki her makineye atanır ve bunları benzersiz şekilde tanımlar.
Adresin bu kısmı benzersiz olmalıdır çünkü bir grup olan ağın aksine belirli bir makineyi (bir bireyi) tanımlar.
Dolayısıyla örnek IP adresi 172.16.30.56'da 30.56 ana bilgisayar adresidir.
The network address—also called the network number—uniquely identifies each network. Every machine on the same network shares that network address as part of its IP address. In the IP address 172.16.30.56, for example, 172.16 is the network address.
The host address is assigned to and uniquely identifies, each machine on a network. This part of the address must be unique because it identifies a particular machine—an individual—as opposed to a network, which is a group. So in the sample IP address 172.16.30.56, the 30.56 is the host address.

## Slide 8: The Hierarchical IP Addressing Scheme
Network addresses are divided into 5 classes:
 | Octet 1 |  |  |  |  |  | Octet 2 | Octet 3 | Octet 4
Class A | 0 | Network ID |  |  |  |  | Host ID |  | 
Class B | 1 | 0 | Network ID |  |  |  |  | Host ID | 
Class C | 1 | 1 | 0 | Network ID |  |  |  |  | Host ID
Class D | 1 | 1 | 1 | 0 | Multicast Address |  |  |  | 
Class E | 1 | 1 | 1 | 1 | Reserved |  |  |  | 
Notes: İnternet tasarımcıları, ağ boyutuna göre ağ sınıfları oluşturmaya karar verdiler.
Çok sayıda ana bilgisayara sahip olan az sayıda ağ için, A sınıfı ağ oluşturdular.
Diğer uçta, az sayıda ana bilgisayara sahip çok sayıda ağ için ayrılan C Sınıfı ağ bulunur.
Ağlar için çok büyük ve çok küçük arasındaki sınıf ayrımı tahmin edilebileceği gibi B Sınıfı ağdır.
Bir IP adresini bir ağa ve ana bilgisayar adresine bölmek, ağınızın sınıf tanımına göre belirlenir.
Aşağıdaki şekil, ağ sınıflarını özetlemektedir.
Verimli yönlendirme sağlamak için, İnternet tasarımcıları, her farklı ağ sınıfı için adresin baştaki bit bölümü için bir yetki tanımladılar.
Örneğin, bir yönlendirici A Sınıfı ağ adresinin her zaman 0 ile başladığını bildiğinden, yönlendirici, adresinin yalnızca ilk bitini okuduktan sonra bir paketin yolunu hızlandırabilir.
Adres şemalarının A Sınıfı, B Sınıfı ve C Sınıfı adres arasındaki farkı tanımladığı yer burasıdır. Bu üç sınıf arasındaki farklar aşağıdaki slaytlarda açıklanacaktır.
The designers of the Internet decided to create classes of networks based on network size. For the small number of networks possessing a very large number of hosts, they created the rank Class A network. At the other extreme is the Class C network, which is reserved for the numerous networks with a small number of hosts. The class distinction for networks between very large and very small is predictably the Class B network. Subdividing an IP address into a network and host address is determined by the class designation of your network. The below figure summarizes the classes of networks.
To ensure efficient routing, Internet designers defined a mandate for the leading-bits section of the address for each different network class. For example, since a router knows that a Class A network address always starts with a 0, the router might be able to speed a packet on its way after reading only the first bit of its address. This is where the address schemes define the difference between a Class A, a Class B, and a Class C address. The differences between these three classes will be explained in the following slides.

## Slide 9: The Hierarchical IP Addressing Scheme
Class A Addresses
Class A Network address is 1-byte long, first bit is always 0
Maximum 27 = 128 Class A networks can be created
Maximum 224 = 16,777,214 hosts (excluding 2 reserved addresses)
First bit is always 0 then
00000000 = 0
01111111 = 127
The addresses 00000000 and 01111111 are reserved for default route and troubleshooting respectively
So Class A network addresses start with 1-126
network
host
host
host
Notes: Örneğin,
49.22.102.70 IP adresinde 49, ağ adresi ve
22.102.70, ana bilgisayar adresidir.
Bu belirli ağdaki her makine, 49'un ayırt edici ağ adresiyle başlayacaktı.
A Sınıfı ağ adresleri 1 bayt uzunluğundadır, bu baytın ilk biti ayrılmıştır ve kalan 7 bit manipülasyon veya adresleme için kullanılabilir.
Sonuç olarak, oluşturulabilecek teorik maksimum A Sınıfı ağ sayısı 128'dir.Diğer 7 bitin hepsini kapatıp açarsak, A Sınıfı ağ adresleri aralığını buluruz.
Yani, A Sınıfı bir ağ ilk sekizlide 0 ile 127 arasında tanımlanır ve daha az veya daha fazla olamaz. İşleri daha da karmaşık hale getirmek için, tüm 0'ların ağ adresi (0000 0000) varsayılan rotayı belirlemek üzere ayrılmıştır. Ek olarak, tanılama için ayrılan 127 adresi de kullanılamaz; bu,
A Sınıfı ağ adreslerini belirlemek için gerçekten yalnızca 1 ila 126 arasındaki sayıları kullanabileceğiniz anlamına gelir. Bu, kullanılabilir A Sınıfı ağ adreslerinin gerçek sayısının 128 eksi 2 veya 126 olduğu anlamına gelir.
Dolayısıyla, bir IP adresinin 128'den az başladığını görürseniz, bunun A Sınıfı bir ağ olduğunu bilirsiniz.
In a Class A network address, the first byte is assigned to the network address, and the three remaining bytes are used for the host addresses.
For example, in the IP address 49.22.102.70, the 49 is the network address and 22.102.70 is the host address. Every machine on this particular network would begin with the distinctive network address of 49.
Class A network addresses are 1 byte long, with the first bit of that byte reserved and the 7 remaining bits available for manipulation, or addressing. As a result, the theoretical maximum number of Class A networks that can be created is 128.
If we turn the other 7 bits all off and then turn them all on, we’ll find the Class A range of network addresses.
So, a Class A network is defined in the first octet between 0 and 127, and it can’t be less or more. To complicate matters further, the network address of all 0s (0000 0000) is reserved to designate the default route. Additionally, the address 127, which is reserved for diagnostics, can’t be used either, which means that you can really only use the numbers 1 to 126 to designate Class A network addresses. This means the actual number of usable Class A network addresses is 128 minus 2, or 126.
So if you see an IP address starts with less than 128 then you know that this is a Class A network.

## Slide 10: The Hierarchical IP Addressing Scheme
Class A Addresses
Address | Function
Network address of all 0s (0.X.X.X) | Means “this network or segment.”
Network address of all 1s (127.X.X.X) | Means “all networks.”
127.0.0.1 | Reserved for loopback tests. Designates the local host and allows that host to send a test packet to itself without generating network traffic.
Host address of all 0s (X.0.0.0) | Means “network address” or any host on the specified network.
Host address of all 1s (X.255.255.255) | Means “all hosts” on the specified network
Entire IP address set to all 0s (0.0.0.0) | Any host on any network
Entire IP address set to all 1s (255.255.255.255) | Broadcast to all hosts on the current network
Notes: "Bu ağ veya segment" anlamına gelir.
"Tüm ağlar" anlamına gelir.
Geridöngü testleri için ayrılmıştır. Yerel ana bilgisayarı belirler ve bu ana bilgisayarın ağ trafiği oluşturmadan kendisine bir test paketi göndermesine izin verir. Geridöngü testleri için ayrılmıştır. Yerel ana bilgisayarı belirler ve bu ana bilgisayarın ağ trafiği oluşturmadan kendisine bir test paketi göndermesine izin verir."
Ağ adresi" veya belirtilen ağdaki herhangi bir ana bilgisayar anlamına gelir.
Belirtilen ağdaki "tüm ana bilgisayarlar" anlamına gelir
Herhangi bir ağdaki herhangi bir ana bilgisayar
Geçerli ağdaki tüm ana bilgisayarlara yayın
Address
Function
Network address of all 0s
(0.X.X.X)
Means “this network or segment.”
Network address of all 1s
(127.X.X.X)
Means “all networks.”
127.0.0.1
Reserved for loopback tests. Designates the local host and allows that host to send a test packet to itself without generating network traffic.
Host address of all 0s
(X.0.0.0)
Means “network address” or any host on the specified network.
Host address of all 1s
(X.255.255.255)
Means “all hosts” on the specified network
Entire IP address set to all 0s (0.0.0.0)
Any host on any network
Entire IP address set to all 1s (255.255.255.255)
Broadcast to all hosts on the current network

## Slide 11: The Hierarchical IP Addressing Scheme
Class B Addresses
Class B Network Address is 2-byte long, first 2 bits are always 10
Maximum 214 = 16,384 Class B networks can be created
Maximum 216 = 65,534 hosts (excluding 2 reserved addresses)
First 2 bits are always 10 then
10000000 = 128
10111111 = 191
Class B Network Addresses start with 128-191
network
network
host
host
Notes: B Sınıfı bir ağ adresinde, ilk 2 bayt ağ adresine atanır ve kalan 2 bayt, ana bilgisayar adresleri için kullanılır.
Örneğin, 172.16.30.56 IP adresinde ağ adresi 172.16 ve ana bilgisayar adresi 30.56'dır.
2 bayt (her biri 8 bit) olan bir ağ adresiyle, 2^16 benzersiz kombinasyonla baş başa kalırız.
Ancak İnternet tasarımcıları, tüm B Sınıfı ağ adreslerinin ikili rakam 1 ve ardından 0 ile başlaması gerektiğine karar verdiler.
Bu, manipüle edilebilecek 14 bitlik konumlar bırakır, bu nedenle gerçekte, 16.384 (yani, 2^14) benzersiz B Sınıfı elde ederiz. ağ adresleri.
B Sınıfı bir ağda, ilk baytın ilk biti her zaman açık, ikinci bit ise her zaman kapalı olmalıdır.
Diğer 6 bitin hepsini kapatıp açarsak,
B Sınıfı bir ağ için aralığı buluruz:10000000 = 12810111111 = 191
Gördüğünüz gibi, ilk bayt 128'den 191'e yapılandırıldığında B Sınıfı bir ağ tanımlanır.
In a Class B network address, the first 2 bytes are assigned to the network address and the remaining 2 bytes are used for host addresses.
For example, in the IP address 172.16.30.56, the network address is 172.16 and the host address is 30.56.
With a network address being 2 bytes (8 bits each), we’re left with 2^16 unique combinations. But the Internet designers decided that all Class B network addresses should start with the binary digit 1, then 0. This leaves 14-bit positions available to manipulate, so in reality, we get 16,384 (that is, 2^14) unique Class B network addresses.
In a Class B network, the first bit of the first byte must always be turned on but the second bit must always be turned off. If we turn the other 6 bits all off and then all on, we will find the range for a Class B network:
10000000 = 128
10111111 = 191
As you can see, a Class B network is defined when the first byte is configured from 128 to 191.

## Slide 12: The Hierarchical IP Addressing Scheme
Class C Addresses
Class C Network Address is 3-byte long, first 3 bits are always 110
Maximum 221 = 2,097,152 Class C networks can be created
Maximum 28 = 254 hosts (excluding 2 reserved addresses)
First 3 bits are always 110 then
11000000 = 192
11011111 = 223
Class C Network Addresses start with 192-223
network
network
network
host
Notes: C Sınıfı bir ağ adresinin ilk 3 baytı, ana bilgisayar adresi için yalnızca 1 bayt kalacak şekilde, adresin ağ bölümüne ayrılmıştır.
192.168.100.102 örnek IP adresi kullanıldığında, ağ adresi 192.168.100 ve ana bilgisayar adresi 102'dir.
C Sınıfı bir ağ adresinde, ilk 3 bit konumu her zaman ikili 110'dur.
Hesaplama şu şekildedir: 3 bayt veya 24 bit, eksi 3 ayrılmış konum, 21 konum bırakır.
Dolayısıyla, 2^21 veya 2.097.152 olası C Sınıfı ağ vardır.
C Sınıfı ağlar için, RFC'ler ilk sekizlinin ilk 2 bitini her zaman açık olarak tanımlar, ancak üçüncü bit asla açık olamaz.
Önceki sınıflarla aynı işlemi izleyerek, aralığı bulmak için ikiliden ondalık sayıya dönüştürün.
İşte bir C Sınıfı ağ aralığı:11000000 = 19211011111 = 223Dolayısıyla, 192 ile 223 arasında bir IP adresi görürseniz, bunun C Sınıfı bir IP adresi olduğunu anlarsınız.
The first 3 bytes of a Class C network address are dedicated to the network portion of the address, with only 1 byte remaining for the host address.
Using the example IP address 192.168.100.102, the network address is 192.168.100 and the host address is 102.
In a Class C network address, the first 3 bit positions are always the binary 110. The calculation is as follows: 3 bytes, or 24 bits, minus 3 reserved positions leave 21 positions. Hence, there are 2^21, or 2,097,152, possible Class C networks.
For Class C networks, the RFCs define the first 2 bits of the first octet as always turned on, but the third bit can never be on. Following the same process as the previous classes, convert from binary to decimal to find the range. Here’s the range for a Class C network:
11000000 = 192
11011111 = 223
So, if you see an IP address with a range from 192 up to 223, you’ll know it’s a Class C IP address.

## Slide 13: The Hierarchical IP Addressing Scheme
Class D Addresses
Not assigned to devices on a network
Used for special-purpose, multicast applications (such as video- and audio-streaming applications)
Need to be registered with IANA to be used globally
First 4 bits are always 1110 then
11100000 = 224
11101111 = 239
Class D Network Addresses start with 224-239
Notes: D Sınıfı ağ adresleri, bir ağdaki cihazlara atanmaz.
Bu adresler, özel amaçlı, çok noktaya yayın uygulamaları (video ve ses akışı uygulamaları gibi) için kullanılır.
Bu adreslerin tümünün küresel olarak kullanılabilmesi için IANA'ya kaydedilmesi gerekir.
Bu sınıftaki adresler, ilk sekizlinin ilk bitlerini 1110'a ayarlayarak, ilk sekizlide 11100000 ila 11101111 veya 224 ila 239 arasında değişen adresler verir.
Bu adresler, normal bir alt ağ maskesi tarafından tanımlanmaz; bunun yerine her adres belirli bir amaç için kullanılır.
Ve her adres ayrı ayrı kullanıldığından 255.255.255.255 maskesi kullanır.
Class D network addresses are not assigned to devices on a network. These addresses are used for special-purpose, multicast applications (such as video- and audio-streaming applications).
These addresses all need to be registered with IANA to be used globally. Addresses in this class have the first bits of the first octet set to 1110, yielding addresses in the first octet ranging from 11100000 to 11101111, or 224 to 239. These addresses are not defined by a normal subnet mask; instead, each address is used for a specific purpose. And because each address is individually used, it uses a 255.255.255.255 mask.

## Slide 14: The Hierarchical IP Addressing Scheme
Class E Addresses
No defined use
Reserved for usage and testing by IANA and the Internet Research Task Force (IRTF)
Need to be registered with IANA to be used globally
First 4 bits are always 1111 then
11110000 = 240
11111111 = 255
Class E Network Addresses start with 240-255
Notes: D Sınıfı ağ adresleri, bir ağdaki cihazlara atanmaz.
Bu adresler, özel amaçlı, çok noktaya yayın uygulamaları (video ve ses akışı uygulamaları gibi) için kullanılır.
Bu adreslerin tümünün küresel olarak kullanılabilmesi için IANA'ya kaydedilmesi gerekir.
Bu sınıftaki adresler, ilk sekizlinin ilk bitlerini 1110'a ayarlayarak, ilk sekizlide 11100000 ila 11101111 veya 224 ila 239 arasında değişen adresler verir.
Bu adresler, normal bir alt ağ maskesi tarafından tanımlanmaz; bunun yerine her adres belirli bir amaç için kullanılır.
Ve her adres ayrı ayrı kullanıldığından 255.255.255.255 maskesi kullanır.
If Class D is special, Class E addresses are even more special. There is no defined use for this address class. Officially, it is listed as reserved for usage and testing by IANA and the Internet Research Task Force (IRTF). In fact, as of RFC3330 in 2002, Class E was updated to “reserved for future use.”
Class E comprises absolutely all valid addresses with 240 or higher in the first octet. The first bits of the first octet is 1111, which yields addresses from 11110000 to 11111110 — or technically, 11111111 — which, in decimals, are 240 to 254 — or 255.
Because this address class is not being used for address allocation, you cannot know what the network ID, which defines the valid addresses in a range, is. So the inclusion of 255 at the end of the range is moot because this address range is not available for you to use. All you need to know is that by definition Class E includes all valid addresses higher than Class D.

## Slide 15: The Hierarchical IP Addressing Scheme
IP Address Classes:
Address Class | 1st Octet Range | 1st Octet Bits | Network & Host Parts | # of Possible Networks # of Hosts per Network
A | 1-127 | 00000000 - 01111111 | N.H.H.H | 128 nets (27) 16,777,214 hosts per net (224)-2
B | 128-191 | 10000000 - 10111111 | N.N.H.H | 16,384 nets (214) 65,534 hosts per net (216)-2
C | 192-223 | 11000000 - 11011111 | N.N.N.H | 2,097,150 nets (221) 254 hosts per net (28)-2
Notes: Bu yönlendirme sorununun çözümü, ağ ve ana bilgisayar veya ağ, alt ağ ve ana bilgisayar tarafından yapılandırılan iki veya üç düzeyli hiyerarşik bir adresleme şeması kullanmaktır.
Bu iki veya üç seviyeli şema, bir telefon numarasına benzer.
İlk bölüm, alan kodu, çok geniş bir alanı belirtir.
İkinci bölüm olan önek, kapsamı yerel bir çağrı alanına daraltır.
Müşteri numarası olan son bölüm, belirli bağlantıyı yakınlaştırır.
IP adresleri aynı tip katmanlı yapıyı kullanır.
Düz adreslemede olduğu gibi, 32 bitin tamamının benzersiz bir tanımlayıcı olarak ele alınması yerine,
adresin bir kısmı ağ adresi olarak belirlenir ve diğer kısım, alt ağ ve ana bilgisayar veya yalnızca ana bilgisayar adresi olarak belirlenir.
The solution to this routing problem is to use a two- or three-level hierarchical addressing scheme that is structured by network and host or by the network, subnet, and host.
This two- or three-level scheme is comparable to a telephone number. The first section, the area code, designates a very large area. The second section, the prefix, narrows the scope to a local calling area. The final segment, the customer number, zooms in on the specific connection. IP addresses use the same type of layered structure. Rather than all 32 bits being treated as a unique identifier, as in flat addressing, a part of the address is designated as the network address and the other part is designated as either the subnet and host or just the host address.

## Slide 16: The Hierarchical IP Addressing Scheme
Private IP Addresses (RFC 1918)
Every host on every network should have a routable IP address. But if every host on every network in the world was required to have an unique IP address, we would have run out of IP addresses!
Notes: Her ağdaki her ana bilgisayarın yönlendirilebilir bir IP adresi olmalıdır.
Ancak, dünyadaki her ağdaki her ana bilgisayarın benzersiz bir IP adresine sahip olması istenseydi, IP adreslerimiz tükenirdi!
İnternetin orijinal tasarımı, her ağdaki her ana bilgisayarın gerçek bir yönlendirilebilir IP adresine sahip olması gerektiğini belirtiyordu.
İnternete erişmek isteyen bir kuruluş, dahili ağını ve üzerindeki ana bilgisayar sayısını açıklayan bazı evrak işlerini tamamlayacaktır.
Kuruluş daha sonra ihtiyaçlarına göre bir dizi IP adresi alacaktır.
Ancak bu kavramla ilgili çok büyük bir sorun vardı - dünyadaki her ağdaki her ana bilgisayarın benzersiz bir IP adresine sahip olması istenseydi, dağıtacak IP adreslerimiz uzun zaman önce tükenmiş olurdu!
The original design of the Internet specified that every host on every network should have a real routable IP address. An organization that wanted to access the Internet would complete some paperwork, describing its internal network and the number of hosts on it. The organization would then receive a number of IP addresses, according to its needs. But there was one huge problem with this concept – if every host on every network in the world was required to have an unique IP address, we would have run out of IP addresses to hand out a long time ago!

## Slide 17: The Hierarchical IP Addressing Scheme
Private IP Addresses (RFC 1918)
The IANA reserved the following IP address blocks for use as private IP addresses:
  Class A: 10.0.0.0 to 10.255.255.255
  Class B: 172.16.0.0 to 172.31.255.255
  Class C: 192.168.0.0 to 192.168.255.255
Notes: Özel IP adresleme kavramı, IP adresi tükenme sorununu çözmek için geliştirilmiştir.
Özel IP adresleri, dünyadaki herhangi bir kuruluşun özel ağında kullanılabilir ve küresel olarak benzersiz değildir.
İnternet yönlendiricileri, özel IP adres aralıklarından gelen paketleri atacak şekilde yapılandırılmıştır, dolayısıyla bu adresler İnternet üzerinde yönlendirilemez.
Aşağıdaki ağı göz önünde bulundurun:Resimde iki kuruluşun kendi iç ağlarında aynı özel IP ağını (10.0.0.0/24) kullandığını görebilirsiniz.
Özel IP adresleri genel olarak benzersiz olmadığından, her iki kuruluş da aynı aralıktaki özel IP adreslerini kullanabilir.
Kuruluşlar, İnternet'e erişmek için sonraki derslerde anlatacağımız Ağ Adresi Çevirisi (NAT) adlı bir teknolojiyi kullanabilir.
The concept of private IP addressing was developed to address the IP address exhaustion problem. The private IP addresses can be used on the private network of any organization in the world and are not globally unique. Internet routers are configured to discard any packets coming from the private IP address ranges, so these addresses are not routable on the Internet.
Consider the following network:
In the picture you can see that two organizations use the same private IP network (10.0.0.0/24) inside their respective internal networks. Because private IP addresses are not globally unique, both organizations can use private IP addresses from the same range. To access the Internet, the organizations can use a technology called Network Address Translation (NAT), which we will describe in the later lessons.

## Slide 18: Introduction to NAT
NAT is a process in which one or more local IP addresses are translated into one or more global IP address and vice versa to provide Internet access to the local hosts
NAT allows multiple devices to access the Internet through a single public address
Notes: NAT, yerel ana bilgisayarlara İnternet erişimi sağlamak için bir veya daha fazla yerel IP adresinin bir veya daha fazla genel IP adresine çevrildiği ve bunun tersi bir işlemdir.NAT, birden fazla cihazın tek bir genel adres aracılığıyla İnternet'e erişmesine izin verirİnternete erişmek için bir genel IP adresi gereklidir, ancak özel ağımızda özel bir IP adresi kullanabiliriz. NAT fikri, birden fazla cihazın tek bir genel adres aracılığıyla İnternet'e erişmesine izin vermektir. Bunu başarmak için, özel IP adresinin genel bir IP adresine çevrilmesi gerekir. Ağ Adresi Çevirisi (NAT), yerel ana bilgisayarlara İnternet erişimi sağlamak için bir veya daha fazla yerel IP adresinin bir veya daha fazla Global IP adresine çevrildiği ve tersinin yapıldığı bir süreçtir. Ayrıca, port numaralarının çevirisini yapar, yani hedefe yönlendirilecek paketteki ana bilgisayarın port numarasını başka bir port numarası ile maskeler. Daha sonra NAT tablosunda karşılık gelen IP adresi ve port numarası girişlerini yapar. NAT genellikle yönlendirici veya güvenlik duvarı üzerinde çalışır.
NAT is a process in which one or more local IP addresses are translated into one or more global IP address and vice versa to provide Internet access to the local hosts
NAT allows multiple devices to access the Internet through a single public address
To access the Internet, one public IP address is needed, but we can use a private IP address in our private network. The idea of NAT is to allow multiple devices to access the Internet through a single public address. To achieve this, the translation of private IP address to a public IP address is required. Network Address Translation (NAT) is a process in which one or more local IP address is translated into one or more Global IP address and vice versa in order to provide Internet access to the local hosts. Also, it does the translation of port numbers i.e. masks the port number of the host with another port number, in the packet that will be routed to the destination. It then makes the corresponding entries of IP address and port number in the NAT table. NAT generally operates on router or firewall.

## Slide 19: Introduction to NAT
Advantages:
  Hides internal structure of the network from the outsider and thus increases network security
  Eliminates address renumbering when a network evolves
  Allows unlimited private IP address range
Disadvantages:
  Changes the IP addresses, thus troubleshooting becomes more complex
  Translation results in switching path delays
  Certain applications will not function while NAT is enabled
  Complicates tunneling protocols such as IPsec
Notes: Avantajlar:NAT, yetkisiz kullanıcılara karşı güçlü bir koruma sağlar, çünkü yetkisiz kullanıcılar NAT'ın arkasındaki sistemlerin hiçbirini görüntüleyemez. İnternetteki diğer sistemlere göre, özel ağın tamamı tek bir sistem, yani NAT sistemi gibi görünür. NAT, özel ağı bilgisayar korsanlarından koruduğu ve bunun gibi bir güvenlik duvarı görevi gördüğü için ağ iletişimi için popüler hale geldi.Bir ağ geliştiğinde adres yeniden numaralandırmayı ortadan kaldırırGenel adresler yalnızca bir bilgisayar İnternet'e bağlandığında gerektiğinden, sınırsız özel IP adresi aralığına izin verir.Dezavantajları:IP adreslerini değiştirir, böylece sorun giderme daha karmaşık hale gelirÇeviri, anahtarlama yolu gecikmelerine neden olurNAT etkinleştirildiğinde belirli uygulamalar çalışmazIPsec gibi tünel protokollerini karmaşık hale getirir
Advantages:
  NAT provides a strong protection against unauthorized users, because unauthorized users cannot view any of the systems behind the NAT. To other systems on the Internet, the entire private network looks like just one system i.e. NAT system. NAT has become popular for networking as it protects the private network from hackers and like this, it also acts as a firewall.
  Eliminates address renumbering when a network evolves
  Allows unlimited private IP address range, as global addresses are required only when a computer is connected to the Internet.
Disadvantages:
  Changes the IP addresses, thus troubleshooting becomes more complex
  Translation results in switching path delays
  Certain applications will not function while NAT is enabled
  Complicates tunneling protocols such as IPsec

## Slide 20: Introduction to NAT
Types of NAT:
Overloading or Port Address Translation (PAT):
  Most popular type of NAT
  Port numbers are used to distinguish the traffic
  Cost-effective as lots of users can be connected by using only one public IP address
Notes: Aşırı yükleme: Bu aynı zamanda NAT aşırı yüklemesi olarak da bilinir. Bunda, birçok yerel (özel) IP adresi, tek bir kayıtlı IP adresine çevrilebilir. Bağlantı noktası numaraları, trafiği, yani hangi trafiğin hangi IP adresine ait olduğunu ayırt etmek için kullanılır. Binlerce kullanıcı yalnızca bir gerçek küresel (genel) IP adresi kullanarak İnternet'e bağlanabileceğinden, bu en sık kullanılan yöntemdir.
Overloading: This is also known as NAT overload. In this, many local (private) IP addresses can be translated to a single registered IP address. Port numbers are used to distinguish the traffic i.e., which traffic belongs to which IP address. This is most frequently used as it is cost-effective as thousands of users can be connected to the Internet by using only one real global (public) IP address.

## Slide 21: IPv4 Address Types
3

## Slide 22: IPv4 Address Types
Layer 2 Broadcasts
Layer 2 broadcast traffic stays within a local area network (LAN) boundary; known as the broadcast domain
A MAC address of FF:FF:FF:FF:FF:FF is used for broadcast
Notes: Bir Katman 2 ağında yayın, bir ağdaki tüm düğümlere trafik gönderme anlamına gelir.Katman 2 yayın trafiği, bir yerel alan ağı (LAN) sınırı içinde kalır; yayın alanı olarak bilinir. Katman 2 yayın trafiği, FF:FF:FF:FF:FF:FF MAC adresi kullanılarak yayın etki alanına gönderilir. Yayın etki alanındaki her cihaz bu MAC adresini tanır ve yayın trafiğini varsa yayın etki alanındaki diğer cihazlara iletir. Yayın, tek noktaya yayın (tek bir düğüme trafik gönderme) veya çok noktaya yayın (bir grup düğüme aynı anda trafik iletme) ile karşılaştırılabilir. IPv4 ile yayınlar oldukça önemlidir, ancak IPv6 ile hiç yayın gönderilmez.
In a Layer 2 network, broadcasting refers to sending traffic to all nodes on a network.
Layer 2 broadcast traffic stays within a local area network (LAN) boundary; known as the broadcast domain. Layer 2 broadcast traffic is sent to the broadcast domain using a MAC address of FF:FF:FF:FF:FF:FF. Every device in the broadcast domain recognizes this MAC address and passes the broadcast traffic on to other devices in the broadcast domain, if applicable. Broadcasting can be compared to unicasting (sending traffic to a single node) or multicasting (delivering traffic to a group of nodes simultaneously).
With IPv4, broadcasts are pretty important, but with IPv6, there aren’t any broadcasts sent at all.

## Slide 23: IPv4 Address Types
Layer 3 Broadcasts
Layer 3 broadcast traffic is sent to all devices in a network
A network address of X.255.255.255 is used for broadcast
Address Resolution Protocol (ARP) uses broadcasting to map MAC addresses to IP addresses
Dynamic Host Configuration Protocol (DHCP) uses broadcasting to dynamically assign IP addresses to hosts
Notes: Katman 3 yayın trafiği, bir yayın ağ adresi kullanılarak bir ağdaki tüm cihazlara gönderilir. Örneğin ağ adresiniz 10.0.0.0 ise yayın ağ adresi 10.255.255.255'tir. Bu durumda, yalnızca 10.0.0.0 ağına ait cihazlar Katman 3 yayın trafiğini alır. Bu ağa ait olmayan cihazlar trafiği düşürür.Adres Çözümleme Protokolü (ARP), MAC adreslerini IP adreslerine eşlemek için yayını kullanır. ARP, IP adresini (mantıksal adres) dinamik olarak doğru MAC adresine bağlar. IP tek noktaya yayın paketleri gönderilmeden önce ARP, IP adresinin yapılandırıldığı Ethernet arabirimi tarafından kullanılan MAC adresini keşfeder.Dinamik Ana Bilgisayar Yapılandırma Protokolü (DHCP), bir ağ segmenti veya alt ağdaki ana bilgisayarlara IP adreslerini dinamik olarak atamak için yayını kullanır.
Layer 3 broadcast traffic is sent to all devices in a network using a broadcast network address. For example, if your network address is 10.0.0.0, the broadcast network address is 10.255.255.255. In this case, only devices that belong to the 10.0.0.0 network receive the Layer 3 broadcast traffic. Devices that do not belong to this network drop the traffic.
Address Resolution Protocol (ARP) uses broadcasting to map MAC addresses to IP addresses. ARP dynamically binds the IP address (the logical address) to the correct MAC address. Before IP unicast packets can be sent, ARP discovers the MAC address used by the Ethernet interface where the IP address is configured.
Dynamic Host Configuration Protocol (DHCP) uses broadcasting to dynamically assign IP addresses to hosts on a network segment or subnet.

## Slide 24: IPv4 Address Types
Unicast Address
Identifies a unique node on a network
Packets addressed to a unicast address are delivered to the node identified by the address
Unicast address has the MAC address of the destination device
Notes: Tek noktaya yayın adresi, bir ağdaki benzersiz bir düğümü tanımlayan bir adrestir. Tek noktaya yayın adresleme, IPv4 ve IPv6'da mevcuttur ve hem gönderme hem de alma için kullanılabilmesine rağmen tipik olarak tek bir göndericiyi veya tek bir alıcıyı ifade eder. Tek noktaya yayın adres paketi, bir arabirim adresi içeren bir ağ düğümüne aktarılır. Tek noktaya yayın adresi daha sonra hedefin ağ cihazı hedefine gönderilen paket başlığına eklenir.Tek noktaya yayın adresi, hedef cihazın MAC adresi değerine sahip olacaktır.
A unicast address is an address that identifies a unique node on a network. Unicast addressing is available in IPv4 and IPv6 and typically refers to a single sender or a single receiver, although it can be used in both sending and receiving.
A unicast address packet is transferred to a network node, which includes an interface address. The unicast address is then inserted into the destination's packet header, which is sent to the network device destination.
The unicast address will have the value of the MAC address of the destination device.

## Slide 25: Internet Protocol Version 6 (IPv6)
4

## Slide 26: Internet Protocol Version 6 (IPv6)
Why do we need IPv6?
Notes: The picture is old already but it shows you the reason why we need IPv6. We are running out of IPv4 addresses!

## Slide 27: Internet Protocol Version 6 (IPv6)
IPv4 4,294,467,295 IP addresses
Class A 16,777,216
Class B 65,535
Class C 256
Large companies (Apple, IBM, Microsoft, etc.) allocated one or more Class A addresses
Many IP addresses are wasted!
Notes: Peki IPv4'e ne oldu? Ne yanlış gitti? Bize 4.294.467.295 IP adresi veren 32 bitimiz var. Class A, B ve C serilerimizi hatırladınız mı? İnternet başladığında, A, B veya C Sınıfı bir ağ elde edersiniz. C Sınıfı size 256 IP adresinden oluşan bir blok verir, B sınıfı 65.535 IP adresi ve A sınıfı hatta 16.777.216 IP adresidir. Apple, Microsoft, IBM ve benzeri büyük şirketler bir veya daha fazla A Sınıfı ağa sahiptir. Gerçekten 16 milyondan fazla IP adresine ihtiyaçları var mıydı? Birçok IP adresi boşa gitti.
So what happened to IPv4? What went wrong? We have 32-bits which gives us 4,294,467,295 IP addresses. Remember our Class A, B and C ranges? When the Internet started you would get a Class A, B or C network. Class C gives you a block of 256 IP addresses, class B is 65.535 IP addresses and class A even 16,777,216 IP addresses. Large companies like Apple, Microsoft, IBM and such got one or more Class A networks. Did they really need more than 16 million IP addresses? Many IP addresses were just wasted.

## Slide 28: Internet Protocol Version 6 (IPv6)
IPv6 is 128-bit long:
340,282,366,920,938,463,463,374,607,431,768,211,456
Enough IP addresses for the entire galaxy!
Notes: IPv6'nın 128 bit adresleri vardır ve 32 bit IPv4'ten çok daha geniş bir adres alanına sahiptir
IPv6 has 128-bit addresses and has a much larger address space than 32-bit IPv4

## Slide 29: Internet Protocol Version 6 (IPv6)
IPv6 is 128-bit long:
340 - undecillion
282 - decillion
366 - nonillion
920 - octillion
938 - septillion
463 - sextillion
463 - quintillion
374 - quadrillion
607 - trillion
431 - billion
768 - million
211 - thousand
456
Notes: IPv6 has 128-bit addresses and has a much larger address space than 32-bit IPv4

## Slide 30: Internet Protocol Version 6 (IPv6)
More Efficient Routing
More Efficient Packet Processing
Directed Data Flows - No broadcasts!
Simplified Network Configuration
Support For New Services - No need for NAT!
Security
Notes: Pv6'yı kullanmaya başlamamızın ana nedeni, daha fazla adrese ihtiyaç duymamızdır, ancak bunun da bazı faydaları vardır:Daha Verimli YönlendirmeIPv6, yönlendirme tablolarının boyutunu azaltır ve yönlendirmeyi daha verimli ve hiyerarşik hale getirir. IPv6 ağlarında parçalanma, yolun maksimum iletim biriminin (MTU) keşfi için bir protokol kullanılarak yönlendirici yerine kaynak cihaz tarafından gerçekleştirilir.Daha Verimli Paket İşlemeIPv6'nın basitleştirilmiş paket başlığı, paket işlemeyi daha verimli hale getirir. IPv4 ile karşılaştırıldığında IPv6, IP düzeyinde sağlama toplamı içermez, bu nedenle sağlama toplamının her yönlendirici atlamasında yeniden hesaplanması gerekmez. Çoğu bağlantı katmanı teknolojisi zaten sağlama toplamı ve hata kontrol yetenekleri içerdiğinden, IP düzeyindeki sağlama toplamından kurtulmak mümkündü. Ek olarak, uçtan uca bağlantıyı yöneten çoğu taşıma katmanı, hata tespitini sağlayan bir sağlama toplamına sahiptir.Yönlendirilmiş Veri AkışlarıIPv6, yayın yerine çok noktaya yayını destekler. Çok noktaya yayın, bant genişliği açısından yoğun paket akışlarının (multimedya akışları gibi) aynı anda birden çok hedefe gönderilmesine izin vererek ağ bant genişliğinden tasarruf sağlar. İlgisiz ana bilgisayarların artık yayın paketlerini işlemesi gerekmez. Ek olarak, IPv6 başlığında, aynı akışa ait paketleri tanımlayabilen Akış Etiketi adlı yeni bir alan bulunur.Basitleştirilmiş Ağ YapılandırmasıOtomatik adres yapılandırması (adres ataması) IPv6'da yerleşiktir. Bir yönlendirici, yönlendirici reklamlarında yerel bağlantının ön ekini gönderir. Bir ana bilgisayar, yerel bağlantı ön ekinin 64 bitine dönüştürülmüş bağlantı katmanı (MAC) adresini ekleyerek kendi IP adresini oluşturabilir.Yeni Hizmetler İçin DestekAğ Adresi Çevirisini (NAT) ortadan kaldırarak, IP katmanındaki gerçek uçtan uca bağlantı geri yüklenerek yeni ve değerli hizmetler sağlanır. Eşler arası ağların oluşturulması ve bakımı daha kolaydır ve VoIP ve Hizmet Kalitesi (QoS) gibi hizmetler daha sağlam hale gelir.GüvenlikGizlilik, kimlik doğrulama ve veri bütünlüğü sağlayan IPSec, IPv6'da yerleşiktir. Kötü amaçlı yazılım taşıma potansiyelleri nedeniyle, IPv4 ICMP paketleri genellikle kurumsal güvenlik duvarları tarafından engellenir, ancak IPSec'in ICMPv6 paketlerine uygulanabilmesi nedeniyle, IPv6 için İnternet Kontrol Mesajı Protokolü'nün uygulanması olan ICMPv6'ya izin verilebilir.
The main reason to start using IPv6 is that we need more addresses but it also has some benefits:
More Efficient Routing
IPv6 reduces the size of routing tables and makes routing more efficient and hierarchical. In IPv6 networks, fragmentation is handled by the source device, rather than the router, using a protocol for discovery of the path's maximum transmission unit (MTU).
More Efficient Packet Processing
IPv6's simplified packet header makes packet processing more efficient. Compared with IPv4, IPv6 contains no IP-level checksum, so the checksum does not need to be recalculated at every router hop. Getting rid of the IP-level checksum was possible because most link-layer technologies already contain checksum and error-control capabilities. In addition, most transport layers, which handle end-to-end connectivity, have a checksum that enables error detection.
Directed Data Flows
IPv6 supports multicast rather than broadcast. Multicast allows bandwidth-intensive packet flows (like multimedia streams) to be sent to multiple destinations simultaneously, saving network bandwidth. Disinterested hosts no longer must process broadcast packets. In addition, the IPv6 header has a new field, named Flow Label, that can identify packets belonging to the same flow.
Simplified Network Configuration
Address auto-configuration (address assignment) is built in to IPv6. A router will send the prefix of the local link in its router advertisements. A host can generate its own IP address by appending its link-layer (MAC) address, converted into the 64 bits of the local link prefix.
Support For New Services
By eliminating Network Address Translation (NAT), true end-to-end connectivity at the IP layer is restored, enabling new and valuable services. Peer-to-peer networks are easier to create and maintain, and services such as VoIP and Quality of Service (QoS) become more robust.
Security
IPSec, which provides confidentiality, authentication and data integrity, is baked into in IPv6. Because of their potential to carry malware, IPv4 ICMP packets are often blocked by corporate firewalls, but ICMPv6, the implementation of the Internet Control Message Protocol for IPv6, may be permitted because IPSec can be applied to the ICMPv6 packets.

## Slide 31: Internet Protocol Version 6 (IPv6)
IP Address representation:
IPv4 51.151.64.242
IPv6 2041:1234:140F:1122:AB91:564F:875B:131B
On browsers:
IPv4: http://51.151.64.242/index.html
IPv6: http://[2041:1234:140F:1122:AB91:564F:875B:131B]/index.html
Octet
Hexadectet
or hextet
Notes: Bir IPv6 adresi neye benziyor? IPv4'ten farklı bir format kullanıyoruz. IPv4'teki gibi ondalık sayılar kullanmıyoruz, artık onaltılık kullanıyoruz. İşte gerçek bir IPv6 adresi örneğiIPv4 adreslerinden bahsettiğimizde, 8 bitlik bir “blok” tanımlamak için “oktet” terimini kullanırız. IPv6'da resmi bir terim (henüz) yoktur ve kullanılacak isimleri tartışan bir IETF taslağı vardır. 4 onaltılık değer için resmi terim "hexadectet"tir, bunun hatırlanması/telaffuz edilmesi zordur, bu nedenle "hextet" kısa biçimi kullanılacaktır.Şimdi görebileceğiniz gibi, adres gerçekten çok daha büyük ve dört yerine sekiz sayı grubuna sahip, ayrıca bu gruplar nokta yerine iki nokta üst üste ile ayrılmış. Belirtilmesi gereken bir diğer şey, test ağınızı IPv6 ile oynayacak şekilde kurduğunuzda, adresi tarayıcıya gerçek adresi parantez içinde yazmanız gerektiğidir. Çünkü iki nokta üst üste, tarayıcı tarafından bir bağlantı noktası numarası belirtmek için zaten kullanılıyor. Dolayısıyla, temel olarak, adresi parantez içine almazsanız, tarayıcının bilgileri tanımlamasının hiçbir yolu olmayacaktır. İşte bunun nasıl göründüğüne bir örnek:
What does an IPv6 address look like? We use a different format than IPv4. We don’t use decimal numbers like for IPv4, we are using hexadecimal now. Here’s an example of an actual IPv6 address
When we talk about IPv4 addresses, we use the term “octet” to define a “block” of 8 bits. In IPv6, there is no official term (yet) and there is an IETF draft that discusses the names to be used. The official term for 4 hexadecimal values is "hexadectet”, this is hard to remember/pronounce so the short form “hextet” will be used.
As you can now see, the address is truly much larger and it has eight groups of numbers instead of four, also that those groups are separated by colons instead of periods. One other thing that should be pointed out is for when you set up your test network to play with IPv6, you have to type the address into the browser with brackets around the literal address. Because a colon is already being used by the browser for specifying a port number. So basically, if you don’t enclose the address in brackets, the browser will have no way to identify the information. Here’s an example of how this looks:

## Slide 32: Internet Protocol Version 6 (IPv6)
Shortening IPv6 Addresses:
Original : 2041:0000:140F:0000:0000:0000:875B:131B
Short : 2041:0000:140F::875B:131B
Original : 2001:0000:0000:0012:0000:0000:1234:56ab
Wrong! : 2001::0012::1234:56AB
You can remove zeros only once!
Notes: IPv6 adresleri onaltılıktır ve 128 bit oldukları için oldukça uzundurlar. Hayatımızı biraz daha iyi hale getirmek için IPv6 adresleri kısaltılabilir.Bir sıfır dizisi varsa, bunları bir kez kaldırabilirsiniz. Yukarıdaki örnekte 0000:0000:0000 bölümünün tamamı kaldırılmıştır. Bunu yalnızca bir kez yapabilirsiniz, böylece bunu yapamazsınız:
IPv6 addresses are hexadecimal and since they are 128-bit, they are quite long. To make our lives a bit better, IPv6 addresses can be shortened.
If there is a string of zeros then you can remove them once. In the example above the entire 0000:0000:0000 part was removed. You can only do this once so you cannot do this:

## Slide 33: Internet Protocol Version 6 (IPv6)
Shortening IPv6 Addresses:
Original : 2041:0000:140F:0000:0000:0000:875B:131B
Short : 2041:0:140F::875B:131B
Original : 2001:0001:0002:0003:0004:0005:0006:0007
Short : 2001:1:2:3:4:5:6:7
Rules:
  An entire string of zeros can be removed, you can only do this once
  4 zeros can be removed, leaving only a single zero
  Leading zeros can be removed
Notes: 4 sıfırlı bir "hextet"iniz varsa, bunları kaldırabilir ve tek bir sıfır bırakabilirsiniz. IPv6 cihazınız kalan 3 sıfırı ekleyecektir.
Baştaki sıfırlar da kaldırılabilir, işte bunu göstermek için başka bir adres:
Bu kuralları özetlemek gerekirse:T
üm bir sıfır dizisi kaldırılabilir, bunu yalnızca bir kez yapabilirsiniz.4 sıfır kaldırılabilir, geriye yalnızca tek bir sıfır kalır.Baştaki sıfırlar kaldırılabilir.
If you have a “hextet” with 4 zeros then you can remove those and leave a single zero. Your IPv6 device will add the remaining 3 zeros.
Leading zeros can also be removed, here’s another address to demonstrate this:
To summarize these rules:
An entire string of zeros can be removed, you can only do this once.
4 zeros can be removed, leaving only a single zero.
Leading zeros can be removed.

## Slide 34: Internet Protocol Version 6 (IPv6)
IPv6 Address Types:
Unicast Address
  Link Local Address: Only valid in local networks. Starts with FE80::/10
  Global Unicast Address: Worldwide unique address. Starts with 2000 to 3FFF
Multicast address - Same as IPv4. Starts with FF00::/8
Anycast Address - Similar to broadcast but instead of sending to all nodes, sends to the closest nodes to sender.
Notes: Tek noktaya yayın adresleri, bir ağ öğesini tam olarak diğer bir öğeyle iletişim kurmak için kullanılır ve iki kategoriye ayrılabilir: bağlantı yerel adresleri ve küresel tek noktaya yayın adresleri.Bağlantı yerel adresleri: Bu kategorideki adresler yalnızca yerel ağlarda geçerlidir ve FE80::/10 biçim ön ekiyle başlar. Yerel bağlantı adresleri, bir yerel ağ içindeki öğeleri adreslemek için kullanılır ve örneğin otomatik yapılandırma için kullanılır. Genel olarak, bir bağlantı yerel adresinin kapsamı bir sonraki yönlendiriciye kadar uzanır, böylece ağa bağlı herhangi bir cihaz onunla iletişim kurarak küresel bir IPv6 adresi oluşturabilir.Küresel tek noktaya yayın adresleri: Küresel tek noktaya yayın adresleri, bir ağ cihazının internete bağlanmak için ihtiyaç duyduğu dünya çapında benzersiz adreslerdir. Biçim öneki genellikle 2000::/3'tür ve 2000 ile 3FFF arasında başlayan tüm adresleri içerir. Küresel tek noktaya yayın adresi yönlendirilebilir ve internet üzerinden yerel ağdaki bir ana bilgisayarı doğrudan adreslemek için kullanılabilir. İnternet sağlayıcılarından son kullanıcılara yeniden dağıtılan küresel tek noktaya yayın adresleri, onaltılık blok 2001 ile başlar.çok noktaya yayın adresleriTek noktaya yayın adresleri bire bir iletişim için kullanılırken, çok noktaya yayın adresleri birden çoğa iletişim uygular. Bununla birlikte distribütör adresleri gelir. Çoklu yayın adresinden gönderilen paketler, çoklu yayın grubunun parçası olan tüm ağ cihazları tarafından alınır. Bir cihaz birden fazla çoklu yayın grubuna ait olabilir. Bir ağ cihazı için bir IPv6 adresi oluşturulursa, tanıma, erişilebilirlik ve önek algılama için gerekli olan belirli çok noktaya yayın gruplarının otomatik olarak üyesi olur. Örneğin, yaygın çok noktaya yayın grupları "tüm yönlendiriciler" veya "tüm ana bilgisayarlar" dır. Çok noktaya yayın adresleri için biçim ön eki genellikle FF00::/8'dir.her noktaya yayın adresleriPaketler, herhangi bir yayın adresinden alıcı gruplarına da gönderilebilir. Yine de, çok noktaya yayın adreslerinden farklı olarak, veri paketleri herhangi bir yayın grubunun tüm üyelerine gönderilmez, yalnızca gönderene en yakın cihaza gönderilir. Anycast adresleri öncelikle yük dağıtımı ve arıza güvenliği amaçları için kullanılır.
Unicast addresses are used to communicate one network element with exactly one other element, and can be divided into two categories: link local addresses and global unicast addresses.
Link local addresses: Addresses in this category are only valid within local networks and begin with the format prefix FE80::/10. Local link addresses are used to address elements within a local network and are used, for example, for auto-configuration. In general, the scope of a link local address extends to the next router, so that any device connected to the network is able to communicate with it to generate a global IPv6 address.
Global unicast addresses: Global unicast addresses are worldwide unique addresses that a network device needs in order to connect to the internet. The format prefix is usually 2000::/3 and includes all addresses that begin with 2000 to 3FFF. The global unicast address is routable and can be used to directly address a host in the local network over the internet. Global unicast addresses, which are redistributed from internet providers to end users, begin with the hexadecimal block 2001.
Multicast addresses
While unicast addresses are used for one-to-one communication, multicast addresses implement a one-to-many communication. Along with this come distributor addresses. Packages that are sent from a multicast address are received by all of the network devices that are part of the multicast group. One device can belong to multiple multicast groups. If an IPv6 address is created for a network device, then it is automatically a member of certain multicast groups that are required for recognition, accessibility, and prefix detection. Common multicast groups, for example, are “all routers” or “all hosts”. The format prefix for multicast addresses is generally FF00::/8.
Anycast addresses
Packages can also be sent to groups of receivers from anycast addresses. Unlike multicast addresses, though, data packages are not sent to all members of an anycast group, but only to the device closest to the sender. Anycast addresses are used primarily for load distribution and failure safety purposes

## Slide 35: Internet Protocol Version 6 (IPv6)
IPv6 Special Addresses:
Address | Meaning
0:0:0:0:0:0:0:0 | Equals ::. The equivalent of IPv4’s 0.0.0.0 and is typically the source address of a host before the host receives an IP address when you’re using DHCP-driven stateful configuration
0:0:0:0:0:0:0:1 | Equals ::1. The equivalent of 127.0.0.1 in IPv4.
2000::/3 | The global unicast address range allocated for Internet access.
FC00::/7 | The unique local unicast range.
FE80::/10 | The link-local unicast range.
FF00::/8 | The multicast range.
3FFF:FFFF::/32 | Reserved for examples and documentation.
2001:0DB8::/32 | Also reserved for examples and documentation.
2002::/16 | Used with 6to4 tunneling, which is an IPv4-to-IPv6 transition system.
Notes: Tablo, sonunda kullanacağınız için kesinlikle hatırlamanız gereken bazı adresleri ve adres aralıklarını listeler. Hepsi özeldir veya belirli bir kullanım için ayrılmıştır, ancak IPv4'ün aksine, IPv6 bize bir adresler galaksisi verir, bu nedenle burada bir ücret ayırmak sorun değildir.
The table lists some of the addresses and address ranges that you should definitely make a point to remember because you’ll eventually use them. They’re all special or reserved for a specific use, but unlike IPv4, IPv6 gives us a galaxy of addresses, so reserving a fe here isn't an issue.

## Slide 36: THANKS!
Any questions?
You can find me at:
@David - Instructor
david@clarusway.com