## Slide 1: Computer Fundamentals

## Slide 2: Were you able to finish pre-class material? Introduction
1
Notes: 🍐 This is a Pear Deck Multiple Choice Slide. Your current options are: A: Yes, B: No,
🍐 To edit the type of question or choices, go back to the "Ask Students a Question" in the Pear Deck sidebar.

## Slide 3: How long did it take to finish it? Introduction
Notes: 🍐 This is a Pear Deck Multiple Choice Slide. Your current options are: A: Couldn't finish, B: Up to 3 hours, C: 3-5 hours, D: More than 5 hours, E: More than 7 hours,
🍐 To edit the type of question or choices, go back to the "Ask Students a Question" in the Pear Deck sidebar.

## Slide 4: Agenda
Introduction
What is Computer
How computers work
Operating Systems
Notes: shortly say

## Slide 5: What is Computer
Notes: feel free to ask
don’t be shy

## Slide 6: What is Computer
Notes: Computers are everywhere, but it's not just desktops and laptops anymore.
Now we have tablets, cell phones, watches, and so much more that perform the same functions.
Question:
1. What are some common features of those devices?
2. Think outside of the box and tell me a computer not in the traditional sense.
Students are challenged to consider what makes a computer a computer, thinking about the common bonds that unify all those things which we call "computers," and also to think outside the box to some things that are computers, but not in the traditional sense. Ultimately our definition of a computer is this: A computer is a device that accepts data or input, and processes it in some way to automatically produce a result.
Desktop computer, nowadays it’s not so popular unless you’re a game enthusiast or need a lot of muscle for the work you do like video editing, design etc.

## Slide 7: What is Computer
Question:
Think outside of the box and tell me a computer not in traditional sense.
Notes: 🍐 This is a Pear Deck Text Slide
🍐 To edit the type of question, go back to the "Ask Students a Question" in the Pear Deck sidebar.

## Slide 8: What is Computer

## Slide 9: What is Computer

## Slide 10: What is Computer

## Slide 11: What is Computer
Notes: 🍐 This is a Pear Deck Multiple Choice Slide. Your current options are: A: Yes, It's a computer., B: No, It's not a computer.,
🍐 To edit the type of question or choices, go back to the "Ask Students a Question" in the Pear Deck sidebar.

## Slide 12: What is Computer
Notes: 🍐 This is a Pear Deck Web Slide.
🍐 To edit the type of question, go back to the "Ask Students a Question" in the Pear Deck sidebar.

## Slide 13: What is Computer

## Slide 14: What is Computer
A computer is…
a device that accepts data or input and store it to somewhere. Then processes this data in someway to automatically produce a result or output.

## Slide 15: How Computers Work
2

## Slide 16
How Computers Work
So how does computers work?
Let’s shop on Apple.com
Notes: How many of you use a mac for the daily use?
Let’s talk
Different companies fundamentals are the same.
Its funny only menus and close button top right top left.
Just to be different
Lets shop for a new computer apple
What kind of buzz words, numbers are there.
3 starting point
What’s the difference between those 3
Lets check technicals.
Be aware of some of the literature
Whats the difference,
Screen size resolution
What might make you feel ok when buying a computer.

## Slide 17
How Computers Work
CHIPS AND TRANSISTORS
1956 Nobel Prize in Physics
Semi-conductor
Cheap
Small
Very low sensitivity
Very low energy consumption
Notes: The Computer Hardware consist of tiny components which called chips.
Chips can contain billions of transistors.
Transistor regulates current or voltage flow and acts as a switch or gate for electronic signals.

## Slide 18
How Computers Work
Central Processing Unit
(Brain of the Computer)
4.6 GHz = 4.6 Billion cycles
per second
Notes: Central Processing Unit, or processor for short. Performs the necessary arithmetic to execute programs.
Almost 1000 holes.
Really small.
Made of silica, sand.
Cpu stays cool with heatsink.
Overheat.
Its important to this cpu stays cool.

## Slide 19
How Computers Work
DATE | CPU | Number of transistors
1972 | Intel 8008 | 3,500
1982 | Intel 80286 | 134,000
1993 | Pentium | 3,100,000
2000 | Pentium 4 | 42,000,000
2012 | Quad-Core + GPU Core i7 | 1,400,000,000
Notes: Central Processing Unit, or processor for short. Performs the necessary arithmetic to execute programs.
Almost 1000 holes.
Really small.
Made of silica, sand.
Cpu stays cool with heatsink.
Overheat.
Its important to this cpu stays cool.

## Slide 20
Temporary
Fast
Expensive
RAM (Random Access Memory)
How Computers Work
Notes: When talking about hardware, memory typically refers to RAM (Random Access Memory).
Short-term memory storage for frequently used programs and instructions to speed up processes.
So we've talked about memory a few times briefly, but it's time to break down the different types of memory. I'm going to use a metaphor using a kitchen for how a computer uses different types of memory.

## Slide 21
Moving Parts
Slow
Cheap
Vulnerable
Hard Drive
How Computers Work
Notes: Long-term storage of programs and files for later usage and access.
Long term storage.
HDD and SSD.
Huge movie collection,
Why do you need a HDD for?
Backup.
Tons of mechanical parts so it can fail.
Solid state drives use flash memory to deliver superior performance and durability. Because there are lots of small, moving parts inside your hard drive — magnetic heads, spindles, and spinning platters — it's easy for things to go wrong and you could lose your important data. Without moving parts, SSDs are more durable, run cooler and use less energy.

## Slide 22
Hard Disk Drive (HDD) vs SSD vs NVMe
How Computers Work

## Slide 23
How Computers Work

## Slide 24: Question: How about NVMe vs RAM? vs
How Computers Work
Notes: 🍐 This is a Pear Deck Multiple Choice Slide. Your current options are: A: RAM is faster., B: NVMe is faster.,
🍐 To edit the type of question or choices, go back to the "Ask Students a Question" in the Pear Deck sidebar.
The difference between SSD and NVMe is that SSD stores data by using integrated circuits while NVMe is an interface used to access the stored data at a high speed. NVMe is far advanced than SSD and hence is faster and better encrypted than the latter.

## Slide 25
How Computers Work
Notes: POWER SUPPLY: We're going to need power to get this computer working.

## Slide 26: GPU (Graphical Processing Unit)
How Computers Work
Notes: The main difference between CPU and GPU architecture is that a CPU is designed to handle a wide-range of tasks quickly (as measured by CPU clock speed), but are limited in the concurrency of tasks that can be running. A GPU is designed to quickly render high-resolution images and video concurrently.
Because GPUs can perform parallel operations on multiple sets of data, they are also commonly used for non-graphical tasks such as machine learning and scientific computation. Designed with thousands of processor cores running simultaneously, GPUs enable massive parallelism where each core is focused on making efficient calculations.
While GPUs can process data several orders of magnitude faster than a CPU due to massive parallelism, GPUs are not as versatile as CPUs. CPUs have large and broad instruction sets, managing every input and output of a computer, which a GPU cannot do. In a server environment, there might be 24 to 48 very fast CPU cores. Adding 4 to 8 GPUs to this same server can provide as many as 40,000 additional cores. While individual CPU cores are faster (as measured by CPU clock speed) and smarter than individual GPU cores (as measured by available instruction sets), the sheer number of GPU cores and the massive amount of parallelism that they offer more than make up the single-core clock speed difference and limited instruction sets.
GPUs are best suited for repetitive and highly-parallel computing tasks. Beyond video rendering, GPUs excel in machine learning, financial simulations and risk modeling, and many other types of scientific computations. While in years past, GPUs were used for mining cryptocurrencies such as Bitcoin or Ethereum, GPUs are generally no longer utilized at scale, giving way to specialized hardware such as Field-Programmable Grid Arrays (FPGA) and then Application Specific Integrated Circuits (ASIC).

## Slide 27
Mainboard or Logic Board
How Computers Work
Notes: Complementary Metal–Oxide–Semiconductor. Small piece of memory that stores the BIOS

## Slide 28
Hard Drive vs RAM
Hard Drive
RAM
CPU
How Computers Work
Notes: Think of the HDD as the refrigerator. It's where the food is stored for later use. There's a lot of space, but running to the fridge every time you need a particular item isn't efficient.

## Slide 29
Input and Output Devices
How Computers Work
Notes: 🍐 This is a Pear Deck Text Slide
🍐 To edit the type of question, go back to the "Ask Students a Question" in the Pear Deck sidebar.
Used for human interaction with hardware and software.
Peripheral
What other input and output methods do we have for computers nowadays?
Voice, touchscreen, keyboard, wireless headphones

## Slide 30
How Computers Work
???
Notes: The input devices for these two software productions are keyboard, microphone. The output devices are speakers, monitor.
Both Cortana and Siri receive inputs and generate outputs, but are not hardware and would not fall into the standard definition of an input/output device.

## Slide 31
How Computers Work
?
Notes: The barcode reader is the input device used with barcodes.

## Slide 32
How Computers Work
Virtual Reality / Augmented Reality / Mixed Reality
Notes: 🍐 This is a Pear Deck Multiple Choice Slide. Your current options are: A: INPUT DEVICE, B: OUTPUT DEVICE, C: BOTH INPUT AND OUTPUT DEVICE,
🍐 To edit the type of question or choices, go back to the "Ask Students a Question" in the Pear Deck sidebar.
ARE THEY INPUT DEVICE OR OUTPUT DEVICES?
Virtual Reality
Augmented Reality
Mixed Reality
AR uses a real-world setting while VR is completely virtual. ... VR requires a headset device, but AR can be accessed with a smartphone. AR enhances both the virtual and real world while VR only enhances a fictional reality.
Gyroscope is an input device.
Augmented Reality (AR) adds digital elements to a live view often by using the camera on a smartphone. Examples of augmented reality experiences include Snapchat lenses and the game Pokemon Go.
Virtual Reality implies a complete immersion experience that shuts out the physical world. Using VR devices such as HTC Vive, Oculus Rift or Google Cardboard, users can be transported into a number of real-world and imagined environments such as the middle of a squawking penguin colony or even the back of a dragon.
Mixed Reality experience combines elements of both AR and VR, where real-world and digital objects interact. Mixed reality technology is just now starting to take off with Microsoft’s HoloLens one of the most notable early mixed reality apparatuses.
Extended Reality (XR) is an umbrella term that covers all of the various technologies that enhance our senses, whether they’re providing additional information about the actual world or creating totally unreal, simulated worlds for us to experience. It includes Virtual Reality (VR), Augmented Reality (AR) and Mixed Reality (MR) technologies.

## Slide 33
How Computers Work
Communication Devices
Network Interface Card
Wireless Adapter
Notes: Basic Input/Output System
Software that initializes hardware and remembers system time.

## Slide 34: Drag your dot to how you are feeling:
Keep going, I understand
I’m a little confused
Stop, I need help!
Notes: Temperature Check
WIth this slide, you can get a quick idea of how your students are feeling about the pace of the lesson. Getting consensus before moving on helps ensure everyone is still with you, and identify the students who might need extra attention.
🍐 This is a Pear Deck Draggable™ Slide.
🍐 To edit the type of question, go back to the "Ask Students a Question" in the Pear Deck sidebar.

## Slide 35
Operating Systems

## Slide 36
Operating Systems
Music
Video
Chat
Shopping
Coding
Reading
Gaming
Notes: Basic Input/Output System
Software that initializes hardware and remembers system time.

## Slide 37
OPERATING SYSTEMS:
AN OPERATING SYSTEM (OS) IS SYSTEM SOFTWARE THAT MANAGES COMPUTER HARDWARE AND SOFTWARE RESOURCES AND PROVIDES COMMON SERVICES FOR COMPUTER PROGRAMS REQUIRE AN OPERATING SYSTEM TO FUNCTION.
Operating Systems
Notes: Software that manages computer hardware and software.
We’re going to load OS from HDD.
Job of the OS is to let you use other computer programs.
Linux, Unix, Windows, Apple.
Even different brands, two different approaches when you power up.
Both fundamentally same. Both just allow you to interact with your computer do some stuff.
Detecting an input from the keyboard,
Sending output to the monitor or tracking files or folders in the storage area,
Controlling peripheral devices such as disk drives and printers,
Running different programs at the same time and not letting interfere with each other,
Checking users if they are authorized or not are some examples of controlling and monitoring system activities.
What about firmware? Firmware is usually fixed but the OS is often updated on a regular basis. Firmware is low-level operations, whereas the OS is high-level interfaces. Firmware is used for a single purpose, but the OS is used for general purposes, which allows any kind of software to run on multiple types of hardware.

## Slide 38
Operating Systems
Notes: Basic Input/Output System
Software that initializes hardware and remembers system time.

## Slide 39
Operating Systems
Kernel:
It connects applications to the actual processing of data. It also manages all communications between software and hardware components to ensure usability and reliability.
Notes: Basic Input/Output System
Software that initializes hardware and remembers system time.
A Kernel is a computer program that is the heart and core of an Operating System. Since the Operating System has control over the system so, the Kernel also has control over everything in the system. It is the most important part of an Operating System. Whenever a system starts, the Kernel is the first program that is loaded after the bootloader because the Kernel has to handle the rest of the thing of the system for the Operating System. The Kernel remains in the memory until the Operating System is shut-down.
The Kernel is responsible for low-level tasks such as disk management, memory management, task management, etc. It provides an interface between the user and the hardware components of the system. When a process makes a request to the Kernel, then it is called System Call.
A Kernel is provided with a protected Kernel Space which is a separate area of memory and this area is not accessible by other application programs. So, the code of the Kernel is loaded into this protected Kernel Space. Apart from this, the memory used by other applications is called the User Space. As these are two different spaces in the memory, so communication between them is a bit slower.

## Slide 40
Operating Systems
BIOS (Basic Input Output System):
It is firmware used to perform hardware initialization during the booting process (power-on startup), and to provide runtime services for operating systems and programs.
Notes: Basic Input/Output System
Software that initializes hardware and remembers system time.
The BIOS includes instructions on how to load basic computer hardware. It includes a test referred to as a POST (Power-On Self-Test) that helps verify the computer meets requirements to boot up properly. If the computer does not pass the POST, you hear a combination of beeps indicating what is malfunctioning in the computer.
POST - Test the computer hardware and make sure no errors exist before loading the operating system.
Bootstrap Loader - Locate the operating system. If a capable operating system is located, the BIOS will pass control to it.
BIOS drivers - Low-level drivers that give the computer basic operational control over your computer's hardware.
BIOS setup or CMOS setup - Configuration program that allows you to configure hardware settings including system settings, such as date, time, and computer passwords.
  CMOS (short for complementary metal-oxide-semiconductor) is the term usually used to describe the small amount of memory on a computer motherboard that stores the BIOS settings. Some of these BIOS settings include the system time and date, as well as hardware settings.
  CMOS can also be referred to as Real-Time Clock (RTC), CMOS RAM, Non-Volatile RAM (NVRAM), Non-Volatile BIOS memory, or complementary-symmetry metal-oxide-semiconductor (COS-MOS).

## Slide 41
Question: What does OS manage?
Operating Systems
Notes: 🍐 This is a Pear Deck Text Slide
🍐 To edit the type of question, go back to the "Ask Students a Question" in the Pear Deck sidebar.
Sending output to the monitor or tracking files or folders in the storage area,
Controlling peripheral devices such as disk drives and printers,
Running different programs at the same time and not letting interfere with each other,
Checking users if they are authorized or not are some examples of controlling and monitoring system activities.

## Slide 42
Operating Systems
Notes: Basic Input/Output System
Software that initializes hardware and remembers system time.
Windows
MacOS
Linux
Ubuntu is the modern, open source operating system on Linux for the enterprise server, desktop, cloud, and IoT.
Android
iOS

## Slide 43
Please write your computers and mobile phones operating system.
Operating Systems
Notes: 🍐 This is a Pear Deck Text Slide
🍐 To edit the type of question, go back to the "Ask Students a Question" in the Pear Deck sidebar.
Sending output to the monitor or tracking files or folders in the storage area,
Controlling peripheral devices such as disk drives and printers,
Running different programs at the same time and not letting interfere with each other,
Checking users if they are authorized or not are some examples of controlling and monitoring system activities.

## Slide 44
Operating Systems
Terminal
Notes: The terminal displays a prompt from the shell

## Slide 45
Operating Systems
Shell
Notes: Shell
The interface to the operating system is called a shell.
The shell is the outermost layer of the operating system. Shells incorporate a programming language to control processes and files, as well as to start and control other programs. The shell manages the interaction between you and the operating system by prompting you for input, interpreting that input for the operating system, and then handling any resulting output from the operating system.
Shells provide a way for you to communicate with the operating system. This communication is carried out either interactively (input from the keyboard is acted upon immediately) or as a shell script. A shell script is a sequence of shell and operating system commands that is stored in a file.
When you log in to the system, the system locates the name of a shell program to execute. After it is executed, the shell displays a command prompt. This prompt is usually a $ (dollar sign). When you type a command at the prompt and press the Enter key, the shell evaluates the command and attempts to carry it out. Depending on your command instructions, the shell writes the command output to the screen or redirects the output. It then returns the command prompt and waits for you to type another command.
A command line is the line on which you type. It contains the shell prompt.

## Slide 46
What do you know about scheduling?
Operating Systems
Notes: 🍐 This is a Pear Deck Text Slide
🍐 To edit the type of question, go back to the "Ask Students a Question" in the Pear Deck sidebar.
The process scheduling is the activity of the process manager that handles the removal of the running process from the CPU and the selection of another process on the basis of a particular strategy. Process scheduling is an essential part of a Multiprogramming operating systems.

## Slide 47
Scheduling:
Multiprogramming
Multiprocessing
Multithreading
Operating Systems
Notes: Core program of the operating system. Handles start-up after BIOS and further input/out requests by software.
Multiprogramming is a method of running multiple programs over a single processor by sharing the processor time in the time sharing environment. While multithreading is the process of running multiple threads to execute concurrently, supported by operating system.
The difference between multiprocessing and multi programming is that Multiprocessing is basically executing multiple processes at the same time on multiple processors, whereas multi programming is keeping several programs in main memory and executing them concurrently using a single CPU only.

## Slide 48
Multiprogramming
Operating Systems
Notes: Core program of the operating system. Handles start-up after BIOS and further input/out requests by software.
Multiprogramming is a rudimentary form of parallel processing in which several programs are run at the same time on a uniprocessor. Since there is only one processor, there can be no true simultaneous execution of different programs.

## Slide 49
Multiprocessing
Operating Systems
Notes: Core program of the operating system. Handles start-up after BIOS and further input/out requests by software.
The running of two or more programs or sequences of instructions simultaneously by a computer with more than one central processor.

## Slide 50
Multithreading
Operating Systems
Notes: Core program of the operating system. Handles start-up after BIOS and further input/out requests by software.
Multithreading is the ability of a program or an operating system process to manage its use by more than one user at a time and to even manage multiple requests by the same user without having to have multiple copies of the programming running in the computer.
Multithreading is a CPU (central processing unit) feature that allows two or more instruction threads to execute independently while sharing the same process resources. A thread is a self-contained sequence of instructions that can execute in parallel with other threads that are part of the same root process.

## Slide 51
What is the difference between processes and threads?
Operating Systems
Notes: 🍐 This is a Pear Deck Text Slide
🍐 To edit the type of question, go back to the "Ask Students a Question" in the Pear Deck sidebar.

## Slide 52
Operating Systems
Files:
Files are spaces on your computer where data is stored.

## Slide 53
Operating Systems
Metadata

## Slide 54
Operating Systems
Metadata

## Slide 55
Operating Systems
File Attributes:
File attributes are metadata associated with computer files that define file system behavior.

## Slide 56
Operating Systems
Directories & Folders

## Slide 57: Drag your dot to how you are feeling:
Keep going, I understand
I’m a little confused
Stop, I need help!
Notes: Temperature Check
WIth this slide, you can get a quick idea of how your students are feeling about the pace of the lesson. Getting consensus before moving on helps ensure everyone is still with you, and identify the students who might need extra attention.
🍐 This is a Pear Deck Draggable™ Slide.
🍐 To edit the type of question, go back to the "Ask Students a Question" in the Pear Deck sidebar.

## Slide 58: THANKS!
Any questions?
You can find me at:
@raymond
raymond@clarusway.com
@Tomy
tomy@clarusway.com